## Slide 1: ParkByDrone
Creators: Alex Beechman, Owen Phelan, Rob Simari
Notes: Speaker: Rob
Park by drone is a service that organizations can use to streamline the parking process at a designated location.

## Slide 2: Problem
Finding an open spot in a crowded parking lot is frustrating and time consuming
For certain businesses, this problem is seemingly unavoidable
  Sports venues are usually downtown and have limited space for parking. Their parking lots will always be partially or completely full on game days
  Airports need to have space for hundreds or even thousands of cars. If the airport is busy, travelers need to search these massive lots for an open spot
There is an obvious need to solve this problem
  Respected news sources use print space on articles related solely to parking spots and how to find them. This means readers must be interested
Notes: Speaker: Rob

## Slide 3: Problem
A Common Solution - Install a system which knows every possible parking space, and has hardware which keeps track of which spaces are available
  Very Expensive – Buying and installing sensors costs a lost of money. Works for hospitals, malls, etc.
An Uncommon Problem – What if parking lots are not used often, but every time they are used, they are incredibly crowded.
  A venue during an event (e.g. Notre Dame parking on game day)
  Airport parking on Thanksgiving
  Non-traditional parking such as parking in fields for festivals and other large events
The common solution is too expensive to be a viable option
ParkByDrone
An Uncommon Solution…
Notes: Speaker: Rob

## Slide 4
Notes: Speaker: nobody

## Slide 5
How it Works
In Theory
The flying field has to be prepped by laying a large blue circle down somewhere.
The location of the flying-field is preprogrammed into the drone. The drone is activated directly via keyboard
The drone takes off, flies above the flying field, and takes a picture
This picture is processed, and the location of the blue circle in the image is identified. The pixel address of the center of this “open spot” is returned.
The drone uses it’s current location and the pixel address to calculate where to fly
The drone flies to this location, hovers for a short period of time, then returns to base
In Practice
Potential Parking Spots are marked
The Drone Flies to the Location
The Drone Take an Image of the Lot
The Drone Identifies the Location of an Open Spot
The Drone flies to the Open Spot
Notes: Speaker: Owen

## Slide 6: Potential Parking Spots are Marked
Can either be a permanent painted shape, or a cheap piece of plastic that is laid down. Either way, very inexpensive.
How it Works
Three potential spots “marked” here
rzf
rzf
rzf
Potential Parking Spots are marked
The Drone Flies to the Location
Notes: Speaker: Owen

## Slide 7: The Drone Flies to the Location
Can either be a permanent painted shape, or a cheap piece of plastic that is laid down. Either way, very inexpensive.
How it Works
Potential Parking Spots are marked
The Drone Flies to the Location
Property Area
rzf
Destination: Parking Lot
rzf
Drone
Notes: Speaker: Owen

## Slide 8: The Drone Takes an Image of the Lot
How it Works
Potential Parking Spots are marked
The Drone Flies to the Location
The Drone Take an Image of the Lot
Image is taken with a GoPro camera, and passed to the drone via a wireless signal from the GoPro
Notes: Speaker: Alex
Explain how taking an image works

## Slide 9: The Drone Identifies the Location of an Open Spot
The Drone first processes the image, then finds the blue circle in the result, then uses the location of the circle to calculate actual coordinates
How it Works
Potential Parking Spots are marked
The Drone Flies to the Location
The Drone Take an Image of the Lot
The Drone Identifies the Location of an Open Spot
1. Get Location in the Image (pixel,pixel)
2. Calculate Actual Location (Lat,Lon)
Notes: Speaker: Rob
Explain how image recognition works

## Slide 10: The Drone Flies to an Open Spot
The drone will remain above the spot until it is filled or a specified amount of time has passed
How it Works
Potential Parking Spots are marked
The Drone Flies to the Location
The Drone Takes an Image of the Lot
The Drone Identifies the Location of an Open Spot
The Drone Flies to the Open Spot
Notes: Speaker: Rob
Explain How Image Recognition Works

## Slide 11: Why ParkByDrone is Pretty Cool
Implementation…... Practical Impact
Drone is not controlled remotely
Object-Oriented Design keeps all image code separate from drone code
Hardware Architecture relies on popular products that communicate with each other
Does not require any on-site hardware
Very low overhead associated with “breaking down” and “setting back up” the system.
Scalability is easy. Just change how drone moves, image code is unchanged.
Easy to find existing codes and methods
Very low cost of testing because each individual product is tested independently
Safety testing easier for same reason
Notes: Speaker: Owen

## Slide 12: Architecture
Raspberry Pi
Drone
GoPro
Send Coordinates
Request Picture
Get Location
Get Picture
Notes: Speaker: Alex
Explain how they all communicate, especially how commands are sent to the goPro and images are received

## Slide 13: Image Processing
1. Raw Image Converted
to HSV
2. Binary mask image
Generate from given color range
3. Mask overlaid with image
Notes: Speaker: Owen